## Slide 1
Aim: Analyze the lifetime of clathrin-coated pit by the exponential fitting
Tracking CCP
Exponential fitting
Analyze contribution and calculate the mean of lifetime
Features:
The trajectories extracted by the tracking software fall into two different categories: trajectories that appear and disappear during the movie; and trajectories that are cut off by the beginning or end of the movie. Therefore, the observed track number was corrected by the probability.
CCP lifetimes range from a few seconds to several minutes. To fully capture this range of dynamics would require image sampling over minutes at a high frame rate. Such exposure leads to significant photobleaching and also substantially impairs cell viability. Two timescale imaging approach was applied by analyzing two datasets with different acquisition frame rates.
(Loerke D, Mettlen M, Yarar D, Jaqaman K, Jaqaman H, Danuser G, et al. (2009) Cargo and Dynamin Regulate Clathrin-Coated Pit Maturation. PLoS Biol 7(3): e1000057. )

## Slide 2
Fast Acquisition 0.643 sec/frame
Slow Acquisition 2.136 sec/frame
Fimg 1
Fimg 2
Get observed tracks by Imaris
FTrack 1
FTrack 2
Fcf Track 1
Time Index
Track duration
Track no. of spots
STrack 1
STrack 2
Track duration
Measured Track no.
Correct factor
Corrected Track no.
Lite Time
Normalized Track population
Simg 1
Simg 2
Correct tracks by probability with Python script
Time Index
Track duration
Track no. of spots
Time Index
Track duration
Track no. of spots
Time Index
Track duration
Track no. of spots
Get observed tracks by Imaris
Correct tracks by probability with Python script
Fcf Track 2
Scf Track 1
Scf Track 2
Track duration
Measured Track no.
Correct factor
Corrected Track no.
Lite Time
Normalized Track population
Track duration
Measured Track no.
Correct factor
Corrected Track no.
Lite Time
Normalized Track population
Track duration
Measured Track no.
Correct factor
Corrected Track no.
Lite Time
Normalized Track population
Merge data from the same acquisition speed
Merge data from the same acquisition speed
Merged Fast F(t)
Merged Slow S(t)
Track duration
Corrected Track no.
Lite Time
Normalized Track population
Track duration
Corrected Track no.
Lite Time
Normalized Track population
dt
dt
Google Colab at hereimntuic@gmail.com
A_Get lifetime probability density function_20241226
Google Colab at hereimntuic@gmail.com
A_Get lifetime probability density function_20241226
Google Colab at hereimntuic@gmail.com
B_Merge tracks from the same acquisition speed.ipynb
Google Colab at hereimntuic@gmail.com
B_Merge tracks from the same acquisition speed.ipynb

## Slide 3
Triple exponential fitting
↓ Lifetime mean
t fmax from F
t smax from
Data wrangling and Lifetime analysis
Column 1
Observed time point t
Column 2
Column 3
Column 4
Histogram merge
Calculate crossing point
Classify trajectories
Calculate relative distribution
Box plot
Google Colab at hereimntuic@gmail.com
C_Normalize Ft and St in Colab_20241229.ipynb

## Slide 4: Parameters of Imaging and Tracking
Imaging with Zeiss Elyra7 TIRF
  Zeiss Elyra7 TIRF
  Pixel size 63*63 nm
  Objective alpha Plan-Apo 63x/1.46 oil
  At ~0.6 sec/ frame and 2 sec/frame
Tracking with Imaris
  Change the frame speed to 1 sec/frame to simplify the calculation. This will be corrected in the Jupyter notebook analysis.
  Image proc\ Gaussian 0.062